## Slide 1: D2d glucose testing update
November 9, 2015

## Slide 2: D2d glucose testing
From start of study: performed at LCBR with exception of New York State samples
  NYS samples tested at our affiliated hospital (University of Vermont Medical Center (UVMMC))
Testing performed on LCBR’s Roche Integra
  Backup plan: UVMMC (Ortho Vitros)
Summer 2015: Changes in Roche performance led to multiple service visits

## Slide 3: LCBR QC / QA
Quality control (QC) at LCBR includes vendor-supplied controls and additional controls.
Additional quality assurance (QA) measures include:
  Periodic testing of aliquots of 20 serum lots to monitor assay performance longitudinally (serum set)
  CLIA-certified; CAP proficiency testing (PT)
  NGSP Level I certification for HbA1c
Glucose testing at our affiliated hospital
  CLIA- and NYS-certified; CAP PT; standard QC/QA
  LCBR sends aliquots from the serum set

## Slide 4: Serum set data

## Slide 5: Serum set data

## Slide 6: LCBR / UVMMC correlation

## Slide 7: LCBR / UVMMC correlation

## Slide 8: LCBR serum, plasma controls

## Slide 9: LCBR / UVMMC correlation: NYS

## Slide 10: LCBR / UVMMC difference plot

## Slide 11: Summary
UVMMC glucose < LCBR glucose
Magnitude of difference = 2.7 - 4.5%
LCBR’s Roche remains down
LCBR is working with EC, CC to address this issue in a manner that best supports D2d.

## Slide 12: D2d glucose testing update
November 9, 2015